## Slide 1: Measuring Instruments and Measurements in Electronics
From Electronics Point of View
his Photo by Unknown author is licensed under CC BY.

## Slide 2: Basic Circuit Measurements
In working on electrical or electronic circuits, you will frequently need to measure voltage, current, or resistance using meters safely and correctly.
The instrument used to measure voltage is a voltmeter
The instrument used to measure current is an ammeter,
The instrument used to measure resistance is an ohmmeter

## Slide 3: Measuring Current in a Circuit

## Slide 4: Measuring Current in a Circuit Cont...
Part (a) shows a simple circuit in which the current through the resistor is to be measured. First make sure the range setting of the ammeter is greater than the expected current and then connect the ammeter in the current path by first opening the circuit, as shown in part (b). Then insert the meter as shown in part (c). Such a connection is a series connection. The polarity of the meter must be such that the current is in at the positive terminal and out at the negative terminal.

## Slide 6: Measuring Voltage in a Circuit
To measure voltage, connect the voltmeter across the component for which the voltage is to be found. Such a connection is a parallel connection. The negative terminal of the meter must be connected to the negative side of the circuit, and the positive terminal of the meter must be connected to the positive side of the circuit

## Slide 7: Measuring Resistance in a Circuit
Click to add text

## Slide 8: Digital Multimeter
A DMM (digital multimeter) is a multifunction electronic instrument that can measure voltage, current, and resistance. DMMs are the most widely used type of electronic measuring instrument.