## Slide 1
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
Computer Communications & Networks
CSNC-2413
N/W Architecture & Application Development
Lec: 3

## Slide 2: Network Architecture
Network communications - a complex task
To deal with this complexity… SIMPLIFY
  comm task divided into modules
  modules arranged in layers
  each layer performs a subset of comm function
  Forms a Network Architecture
    multiple layers
    each layer has one/more Protocols
    protocols perform specific comm tasks
    provide/obtain services to/from higher/lower layer
Notes: The long-distance carrier system provided in the United States and throughout the world was designed to transmit voice signals over high-capacity transmission links, such as optical fiber, coaxial cable, and microwave. Part of the evolution of these telecommunications networks to digital technology has been the adoption of synchronous TDM transmission structures. In the United States, AT&T developed a hierarchy of TDM structures of various capacities; this structure is used in Canada and Japan as well as the United States. A similar, but unfortunately not identical, hierarchy has been adopted internationally under the auspices of ITU-T.
The basis of the TDM hierarchy (in North America and Japan) is the DS-1 transmission format. The same DS-1 format is used to provide both multiplexed voice and digital data services. Above the DS-1 data rate of 1.544 Mbps, higher-level multiplexing is achieved by interleaving bits from DS-1 inputs. For example, the DS-2 transmission system combines four DS-1 inputs into a 6.312-Mbps stream. Data from the four sources are interleaved 12 bits at a time. Note that 1.544  4 = 6.176 Mbps. The remaining capacity is used for framing and control bits.

## Slide 3: Network Architecture
Example of a layered network system
Network Architecture
A structured set of protocols to implement the communications function
application
transport
network
link
physical

## Slide 4: Internet protocol stack
Application: support applications (network API)
  FTP, SMTP, HTTP, DNS, DHCP
Transport: process-process data transfer (ports)
  TCP (reliable), UDP (unreliable)
Network: global addressing (IP addr), routing of pkts from src to dest
  IPv4, IPv6
Link: data transfer between neighboring network elements
  Ethernet, WiFi (802.11), 3G/4G, PPP
Physical: bits “on the wire”
application
transport
network
link
physical

## Slide 5: TCP/IP Model
Some of the protocols & networks in TCP/IP protocol stack…
Ethernet
WiFi
PPP
3G/4G
HTTP
FTP
SMTP
DNS

## Slide 6
Encapsulation
Data generated by Appl layer
When being sent, each layer appends its header
When being received, each layer removes its header
Principle of Encapsulation & Decapsulation

## Slide 7: Why Layered Architecture
Network Architecture - layered architecture
  provides modularity
    changes in one layer do not require changes in other layers
    simplifies system maintenance & upgradation
  facilitates process of network evolution
    allows to change/improve underlying technologies, with increase in application demands
Notes: The long-distance carrier system provided in the United States and throughout the world was designed to transmit voice signals over high-capacity transmission links, such as optical fiber, coaxial cable, and microwave. Part of the evolution of these telecommunications networks to digital technology has been the adoption of synchronous TDM transmission structures. In the United States, AT&T developed a hierarchy of TDM structures of various capacities; this structure is used in Canada and Japan as well as the United States. A similar, but unfortunately not identical, hierarchy has been adopted internationally under the auspices of ITU-T.
The basis of the TDM hierarchy (in North America and Japan) is the DS-1 transmission format. The same DS-1 format is used to provide both multiplexed voice and digital data services. Above the DS-1 data rate of 1.544 Mbps, higher-level multiplexing is achieved by interleaving bits from DS-1 inputs. For example, the DS-2 transmission system combines four DS-1 inputs into a 6.312-Mbps stream. Data from the four sources are interleaved 12 bits at a time. Note that 1.544  4 = 6.176 Mbps. The remaining capacity is used for framing and control bits.

## Slide 8: Some network apps
e-mail
web surfing
search engine
P2P file sharing
text messaging
social networking
remote login
streaming stored video (YouTube, Netflix)
IP radio, TV
multi-user N/W games
voice over IP (Skype, viber)
real-time video conferencing
…..
How these appls are created…

## Slide 9: Creating network apps
Write appl programs to run only on end systems
appl comm over N/W
web browser comm with server
No need to write software for network-core devices…
network-core devices function at lower layers
confining appls to end systems allows rapid appl development & deployment
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 10: Application architectures
Possible structures of applications:
client-server
peer-to-peer (P2P)

## Slide 11: Client-server architecture
Servers
always-on host
permanent addr (IP & port)
rely on fixed infra-structure
data centers for scaling
Clients
request services from servers
intermittent host connections
dynamic addr (IP & port)
no direct comm with each other
client/server

## Slide 12: P2P architecture
NO always-on server
  arbitrary end systems comm directly
peers request services from other peers, & also provide services
Self Scalability
  new peers bring new service demands
  also add new service capacity
Complex Management
  peers connect intermittently
  change IP addrs
min, or no reliance, on infra-structure
peer-peer

## Slide 13: Architectural Challenges
Client Server
Infra-structure intensive
Cost of server hardware, software & access network B/W
System management needs/costs
May become a bottleneck
P2P
Not ISP friendly; require high upload B/W
Security issues
Incentives; users need to volunteer storage, bandwidth & computation resource

## Slide 14: How do Appls comm
Appls within same host
  processes usually comm using IPC (Inter Process Comm)
  use Pipes, FIFOs, shared memory
Applications are processes running on hosts…
Appls in distant hosts
  processes comm by exchanging messages
  Use sockets, RPC

## Slide 15: Next few slides will help you for labs also consider them part of theory

## Slide 16: Sockets
Remote processes comm thru sockets…
Socket : “software interface between process & N/W”
Process sends/receives msgs to/from its socket
  process reads/writes the socket to receive/send msgs

## Slide 17: Process Address
to receive msgs, process must have identifier
host device has unique IP address (32 bits)
  but many processes may run on same host
  need another level of identifier – Port No (16 bits)
identifier includes both IP address & port number associated with a process on a host…
  Socket address
  IP addr + Port No
to send HTTP msg to web server gaia.cs.umass.edu…
  IP address: 128.119.245.12 port number: 80

## Slide 18: Socket Programming
Allows network applications to communicate across an Internet
Socket API mainly provides Transport layer service interface
    Stream-sockets for TCP
    Datagram-sockets for UDP
Based on client/server architecture
Socket Interface
TCP
UDP
IP
Network Access

## Slide 19: Client/Server functions
Client / Server may run on same or different hosts
Client makes Request…
  sends message to server to perform a task
Server Responds…
  performs task & sends back reply
Client
process
Server
process
1. Client sends request
2. Server
handles
request
3. Server sends response
4. Client
handles
response
Resource
Notes: Both Can run on the same machine

## Slide 20: Servers / Services
Servers : long-running application processes (daemons)
  typically created at boot-time by OS
  run continuously in background
  web server, or mail server
Server waits for requests on a well-known port associated with a particular service
  Port 7: echo server
  Port 23: telnet server
  Port 25: mail server
  Port 53: DNS server
  Port 80: HTTP server
/etc/services provides list of available services (Linux machine)

## Slide 21: Clients
Client – appl launched to access some service, mostly on remote system
  web browser, ftp client, telnet client, ssh client
Client does not need well known port
  usually assigned ephemeral port by kernel
  can also be selected by application
Server - need not know client location
Client - needs to know server location (port + IP address)

## Slide 22: Socket
Socket is an endpoint of bidirectional comm…
  identified by socket descriptor
Clients & Servers comm with each other thru sockets
  open a socket
  write data to socket
  read data from socket
App
socket
3
2
1
Dest.

## Slide 23: Socket Address
The pair IP Address + Port -– makes up a “socket-address”
Server
Client
Client socket address
128.2.194.242:3479
Server socket address
208.216.181.15:53
Client IP address
128.2.194.242
Server IP address
208.216.181.15
3479 is an
ephemeral port allocated by kernel (unix)
53 is a well-known port associated with DNS servers

## Slide 24: TCP & UDP Ports
TCP and UDP port numbers ranges:
  values 0 – 216 (65,536 ports)
  Internet Assigned Numbers Authority (IANA)
Well Known Ports (0 - 1023)
  used by system processes for well known services
  HTTP: 80, E-mail: 25, DNS: 53
Registered Ports (1024 - 49151)
  used by vendors for common applications
  Web Proxy: 8080, IPSec: 1293, Kaaza: 1214
Dynamic or Ephemeral Ports (49152 - 65535)
  used by clients
  automatically allocated by kernel on temporary basis