## Slide 1
Image Enhancement (Point Processing)
Dr Muhammad Zubair
1

## Slide 2
In this lecture we will look at image enhancement point processing techniques:
  Connectivity & Relationship b/w Pixels
  What is Image Processing
  What is point processing?
  Negative images
  Thresholding
  Logarithmic transformation
  Power law transforms
  Grey level slicing
  Bit plane slicing
Contents
Notes: 2

## Slide 3
Process an image to make the result more suitable than the original image for a specific application
–Image enhancement is subjective (problem /application oriented)
Image enhancement methods:
Spatial domain: Direct manipulation of pixel in an image (on the image plane)
Frequency domain: Processing the image based on modifying the Fourier transform of an image
Many techniques are based on various combinations of methods from these two categories
3
What is Image Enhancement

## Slide 4
Relationship Between Pixels

## Slide 5
Establishing boundaries of objects and components of regions in an image.
Group the same region by assumption that the pixels being the same color or equal intensity will have the same region
Two pixels may be four neighbors, but they are said to be connected only if they have the same value (gray level)
Connectivity

## Slide 6
6
Basic Relationship b/w Pixels

## Slide 7
7
Basic Relationship b/w Pixels

## Slide 8
8
Basic Relationship b/w Pixels

## Slide 9
9
Basic Relationship b/w Pixels

## Slide 10
So far when we have spoken about image grey level values we have said they are in the range [0, 255]
  Where 0 is black and 255 is white
There is no reason why we have to use this range
  The range [0,255] stems from display technologes
For many of the image processing operations in this lecture grey levels are assumed to be given in the range [0.0, 1.0]
A Note About Grey Levels
Notes: 10

## Slide 11
Image enhancement is the process of making images more useful
The reasons for doing this include:
  Highlighting interesting detail in images
  Removing noise from images
  Making images more visually appealing
What Is Image Enhancement?
Notes: 11

## Slide 12
Image Enhancement Examples
Notes: 12

## Slide 13
Image Enhancement Examples (cont…)
Notes: 13

## Slide 14
Image Enhancement Examples (cont…)
Notes: 14

## Slide 15
Image Enhancement Examples (cont…)
Notes: 15

## Slide 16
There are two broad categories of image enhancement techniques
  Spatial domain techniques
    Direct manipulation of image pixels
  Frequency domain techniques
    Manipulation of Fourier transform or wavelet transform of an image
For the moment we will concentrate on techniques that operate in the spatial domain
Spatial & Frequency Domains
Notes: 16

## Slide 17
Process an image to make the result more suitable than the original image for a specific application
–Image enhancement is subjective (problem /application oriented)
Image enhancement methods:
Spatial domain: Direct manipulation of pixel in an image (on the image plane)
Frequency domain: Processing the image based on modifying the Fourier transform of an image
Many techniques are based on various combinations of methods from these two categories
Image Engancement

## Slide 18
18
Image Enhancement

## Slide 19
Spatial domain enhancement methods can be generalized as
g(x,y)=T[f(x,y)]
f(x,y): input image
g(x,y): processed (output) image
T[*]: an operator on f (or a set of input images), defined over neighborhood of (x,y)
Neighborhood about (x,y): a square or rectangular sub-image area centered at (x,y)
19
Some Basic Concepts

## Slide 20
20
Some Basic Concepts

## Slide 21
g(x,y) = T [f(x,y)]
Pixel/point operation:
Neighborhood of size 1x1: g depends only on f at (x,y)
T: a gray-level/intensity transformation/mapping function
Let r = f(x,y) s = g(x,y)
r and s represent gray levels of f and g at (x,y)
Then s = T(r)
Local operations:
g depends on the predefined number of neighbors of f at (x,y)
Implemented by using mask processing or filtering
Masks (filters, windows, kernels, templates) :
a small (e.g. 3×3) 2-D array, in which the values of the
coefficients determine the nature of the process
Some Basic Concepts

## Slide 22
The simplest spatial domain operations occur when the neighbourhood is simply the pixel itself
In this case T is referred to as a grey level transformation function or a point processing operation
Point processing operations take the form
s = T ( r )
where s refers to the processed image pixel value and r refers to the original image pixel value
Point Processing
Notes: 22

## Slide 23
23
Image Negatives
Log Transformations
Power-Law Transformations
Common Pixel Operations

## Slide 24
Negative images are useful for enhancing white or grey detail embedded in dark regions of an image
  Note how much clearer the tissue is in the negative image of the mammogram below
Point Processing Example: Negative Images
Original Image
Negative Image
Notes: 24

## Slide 25
Negative Images

## Slide 26
Point Processing Example: Negative Images (cont…)
Original Image
x
y
Image f (x, y)
Enhanced Image
x
y
Image f (x, y)
s = intensitymax - r
For L gray levels the transformation function is
s =T(r) = (L - 1) - r
Notes: 26

## Slide 27
Thresholding transformations are particularly useful for segmentation in which we want to isolate an object of interest from a background
Point Processing Example: Thresholding
s =
255
0
r <= threshold
r > threshold
Notes: 27

## Slide 28
Point Processing Example: Thresholding

## Slide 29
Point Processing Example: Thresholding (cont…)
Original Image
x
y
Image f (x, y)
Enhanced Image
x
y
Image f (x, y)
s =
0 r <= threshold
255 r > threshold
Notes: 29

## Slide 30
Intensity Transformations

## Slide 31
There are many different kinds of grey level transformations
Three of the most common are shown here
  Linear
    Negative/Identity
  Logarithmic
    Log/Inverse log
  Power law
    nth power/nth root
Basic Grey Level Transformations
Notes: 31

## Slide 32
s =T(r) = a.r (a is a constant)
Image Scaling

## Slide 33
Image Scaling

## Slide 34
The general form of the log transformation is
s = c * log(1 + r)
The log transformation maps a narrow range of low input grey level values into a wider range of output values
The inverse log transformation performs the opposite transformation
Log functions are particularly useful when the input grey level values may have an extremely large range of values
Logarithmic Transformations
Notes: 34

## Slide 35
Logarithmic Transformations (cont…)

## Slide 36
08/01/2018
36
Properties of log transformations
–For lower amplitudes of input image the range of gray levels is expanded
–For higher amplitudes of input image the range of gray levels is compressed
Application:
  This transformation is suitable for the case when the dynamic range of a processed image far exceeds the capability of the display device (e.g. display of the Fourier spectrum of an image)
  Also called “dynamic-range compression / expansion”
Logarithmic Transformations

## Slide 37
Logarithmic Transformations (cont…)
Original Image
x
y
Image f (x, y)
Enhanced Image
x
y
Image f (x, y)
s = log(1 + r)
We usually set c to 1
Grey levels must be in the range [0.0, 1.0]
Notes: 37

## Slide 38
Power law transformations have the following form
s = c * r γ
c & γ must be positive
Map a narrow range of dark input values into a wider range of output values or vice versa
Varying γ gives a whole family of curves
Power Law Transformations
Notes: 38

## Slide 39
We usually set c to 1
Grey levels must be in the range [0.0, 1.0]
Power Law Transformations (cont…)
Original Image
x
y
Image f (x, y)
Enhanced Image
x
y
Image f (x, y)
s = r γ
Notes: 39

## Slide 40
For γ < 1: Expands values of dark pixels, compress values of brighter pixels
For γ > 1: Compresses values of dark pixels, expand values of brighter pixels
If γ=1 & c=1: Identity transformation (s = r)
A variety of devices (image capture, printing, display) respond according to power law and need to be corrected
Gamma (γ) correction
The process used to correct the power-law response phenomena
Power Law Transformations (cont…)

## Slide 41
Power Law Example
Notes: 41

## Slide 42
Power Law Example (cont…)
γ = 0.6
Notes: 42

## Slide 43
Power Law Example (cont…)
γ = 0.4
Notes: 43

## Slide 44
Power Law Example (cont…)
γ = 0.3
Notes: 44

## Slide 45
The images to the right show a magnetic resonance (MR) image of a fractured human spine
Different curves highlight different detail
Power Law Example (cont…)
Notes: 45
The third transform is a step too far

## Slide 46
Power Law Example
γ = 1.0
Notes: 46

## Slide 47
Power Law Example (cont…)
γ = 3.0

## Slide 48
Power Law Example (cont…)
γ = 4.0

## Slide 49
Power Law Example (cont…)
γ = 5.0
Notes: 49

## Slide 50
An aerial photo of a runway is shown
This time power law transforms are used to darken the image
Different curves highlight different detail
Power Law Transformations (cont…)
Notes: 50

## Slide 51
51
Power Law Transformations (cont…)

## Slide 52
Gamma Correction
Problem: CRT display devices do not respond linearly to different intensities

## Slide 53
More Contrast Issues

## Slide 54
More Contrast Issues

## Slide 55
Piecewise Linear Transformation
Contrast Stretching
Goal:
  Increase the dynamic range of the gray levels for low contrast images
Low-contrast images can result from
–poor illumination
–lack of dynamic range in the imaging sensor
–wrong setting of a lens aperture during image acquisition
Notes: 55

## Slide 56
Contrast Stretching

## Slide 57
57
Contrast Stretching

## Slide 58
Highlights a specific range of grey levels
  Similar to thresholding
  Other levels can be suppressed or maintained
  Useful for highlighting features in an image
Gray Level Slicing
Notes: 58

## Slide 59
Often by isolating particular bits of the pixel values in an image we can highlight interesting aspects of that image
  Higher-order bits usually contain most of the significant visual information
  Lower-order bits contain subtle details
Bit Plane Slicing
Notes: 59

## Slide 60
Bit Plane Slicing (cont…)
[10000000]
[01000000]
[00100000]
[00001000]
[00000100]
[00000001]
Notes: 60

## Slide 61
Bit Plane Slicing (cont…)
Notes: 61

## Slide 62
Bit Plane Slicing (cont…)
Notes: 62

## Slide 63
Bit Plane Slicing (cont…)
Notes: 63

## Slide 64
Bit Plane Slicing (cont…)
Notes: 64

## Slide 65
Bit Plane Slicing (cont…)
Notes: 65

## Slide 66
Bit Plane Slicing (cont…)
Notes: 66

## Slide 67
Bit Plane Slicing (cont…)
Notes: 67

## Slide 68
Bit Plane Slicing (cont…)
Notes: 68

## Slide 69
Bit Plane Slicing (cont…)
Notes: 69

## Slide 70
Bit Plane Slicing (cont…)
Notes: 70

## Slide 71
Bit Plane Slicing (cont…)
Reconstructed image using only bit planes 8 and 7
Reconstructed image using only bit planes 8, 7 and 6
Reconstructed image using only bit planes 7, 6 and 5
Notes: 71

## Slide 72
A Different Problem

## Slide 73
Lets Double the Size

## Slide 74
Interpolation
Nearest Neighbor

## Slide 75
What Happens When Tripling

## Slide 76
Is There a Better Method
Interpolation: Bi-Linear

## Slide 77
Is There be a Better Method

## Slide 78
What Happens in 2D

## Slide 79
Which is Better

## Slide 80
Which is Better
Lets Scale
Before Interpolation
Nearest Neighbor
Bi-Linear
Original

## Slide 81
No Interpolation
Fast as No Processing Required
Depends on only 2 Pixel
Results are Blocky
Cannot Create New Values
Not Recommended for Smooth Data
New Value always inside the boundary range
Interpolated
Slow due to Processing
Depends on 4 or more pixels
Smoother Gradients
Can Find New Values
Not Recommended for Categorical Data
Value may or May not be outside the boundary range

## Slide 82
We have looked at different kinds of point processing image enhancement
Assignment & Quiz
Bring Your Laptops on Monday?
Next time we will start to look at Global Operations
Summary
Notes: 82